## Slide 1: TELEMETRY SYSTEM
Creating a live measuring and communication system
Lucas PRIEELS

## Slide 2: TELEMETRY SYSTEM
Very limited measurements
  Motor current
  Motor voltage
  Potentiometer value
No live communication
  Only stored on an SD card
Status from last year

## Slide 3: TELEMETRY SYSTEM
Goals
Connect additional sensors
  Power and energy used by motor
  GPS position of the car
  Speed of the car
Create a live communication system
Receive and show data live

## Slide 4: TELEMETRY SYSTEM
Choice of sensors
Accelerometer
  Measures acceleration and (estimated) speed
  Price, precision, refresh rate, 3-axis
GPS sensor
  Measures position, speed, and time
  Price, power usage, compatible with multiple GNSS, configuration time
Current and voltage sensors
  Updated by the powertrain team with the buck converter
SD card
  Same as last year

## Slide 5: TELEMETRY SYSTEM
Wireless communication
Cellular communication (GSM/3G, or NB-IoT/LTE-M)
  Needs connection to a base station
  Unlimited range
  GSM, 3G : Large power consumption
  SD card and cellular subscription
  Very large data rate
Radio communication
  2 components required
  Range might be a bit short
  Legal restrictions on power emission
Radio communication chosen for power usage and coverage reasons
  Arduino MKR WAN 1300/1310 : LoRa, acts as a uc, quite immune to interference, power consumption settable

## Slide 6: TELEMETRY SYSTEM
Overview

## Slide 7: TELEMETRY SYSTEM
Implementation
Electrical connections
Programming of the boards
UART, SPI and I2C connections
Derived calculations
  Electrical power and energy usage
  Smooth speed
  Average speed
  Distance traveled

## Slide 8: TELEMETRY SYSTEM
Real-time data processing

## Slide 9: TELEMETRY SYSTEM
Conclusion
Functionalities
  Measurements performed : position, speed, current voltage, pedal pressing
  Derived values : energy, power, distance traveled, average speed
  All measurements stored on an SD card
  Sent wirelessly
  Data analyzed and plotted in real-time
Possible improvements
  In-depth analysis of data to define a driving strategy
  Send data to the driver